## Slide 1
Robust Control in Real Time Reinforcement Learning Using Adaptive Response Times
Devdhar Patel1, Francesca Walsh1, Zhongyang Zhang1, Tauhidur Rahman1, Terrence Sejnowski2, Hava Siegelmann1
1University of Massachusetts Amherst, Amherst MA
2 Salk Institute for Biological Studies, La Jolla, CA
Introduction
In a real-time environment, there is delay between the input and actuation.
We modified the inverted pendulum task to add a horizontal perturbation force of random intensity, direction and at random times.
For standardized evaluation, perturbation was added every five seconds of increasing intensity until the agent failed.
We augmented a feed forward neural network with a fast three-neuron reflex loop so that the reflex can react faster than the original network.
The reflex is not learned and is hardcoded.
Traditional RL
Real-time RL
s0
a0
s1
a1
a2
s2
a1
a2
No action
a0
a0
a1
a2
s0
a0
s1
a1
s2
a2
s3
Environment paused
Environment simulating
s0
s1
s2
s1
s2
s3
Environment simulation
Agent Processing
Slow response
Fast Reflex: three neurons
Input
Task: Modified Inverted Pendulum
Diagram adapted from Kandel et. al (2015) p.763
Our Biologically Inspired Reflex Architecture
Biological Reflex Loop – Leg Withdrawal from Nociceptive Stimuli
Results Overview
The optimal response time differs based on the environment and constrains such as memory, network capacity and energy.
When augmented with reflexes, the network is more robust to perturbation and survives longer in the environment.
Slower networks with reflex outperform faster networks without reflexes saving compute, memory and energy.
Response Time vs Performance
Chart: Performance w/wo reflexes
| 0.16s | 0.08s | 0.04s | 0.02s | 0.01s
Without Reflex | 83.81 | 109.21 | 127.8 | 152.68 | 138.4
Reflex | 107.72 | 115.41 | 132.23 | 159.63
Future work:
Integrate reflexes into adaptive actor-critic architecture where the actor’s response time is modulated by the critic using the TD-error (Dopamine).
High TD-error results in a surprise which causes the actor to increase its response speed and pay more temporal attention.
Low TD-error causes boredom and allows the actor to decrease its speed thus reducing temporal attention and saving energy.
Future work: Modulate response time using TD-error (Dopamine)
 | Seconds survived (Decisions made) |  |  |  | 
Res. speed | 0.16s | 0.08s | 0.04 | 0.02 | 0.01
w/o Reflex | 83.81 (534) | 109.21 (1366) | 127.8 (3195) | 152.68 (7634) | 138.4 (13840)
Reflex | 107.72 (674) | 129.14 (1618) | 132.23 (3306) | 159.63 (7982) |